## Slide 1: Access Privileges + System Calls
07/04/2021

## Slide 2: Overview
Some resources are restricted
  e.g. printf()
Two operating modes provided by the machine (HW)
  Supervisory
  Non-Supervisory
    Under this is PL/PAL (privileged) and NPL/NPAL (nonprivileged)
  Control register changes mode
  Status register maintains the current mode

## Slide 3: Operating Modes (in detail)
Supervisory
  if any interrupts are executed, microprocessor indicates supervisory
  Access level must be PL only
Non-Supervisory
if any user programs are executed, microprocessor indicates non-supervisory
  Program only has access to it’s own chunk of memory
  ACCESS PRIVILEGE LEVEL:
    PL:
    NPL:
  Always in PL at first before OS changes the program lvl for user programs.
  Access can only go down
    Exception: System Calls (and HW interrupts)

## Slide 4: System Call Steps
fnc called {
  SW interrupt generated;
  }
Interrupt Vector Table is accessed and HW changes PC to the first line of the corresponding ISR (remember the OS contains all of the ISR’s in RAM)
Now, in supervisory mode, change privilege level to PL since this is a user pgm.
ISR returns and the PC returns back to initial fnc
SW step that needed the PL mode is done
Mode changes back into NPL